## Slide 1: Towards Accurate Accounting of Cellular Data for TCP Retransmission
Younghwan Go, Denis Foo Kune*, Shinae Woo,
KyoungSoo Park, and Yongdae Kim
KAIST University of Massachusetts Amherst*
HotMobile’13, Jekyll Island, GA, USA
Notes: Good morning. My name is Younghwan Go, I’m going to talk about whether we should account for TCP retransmissions in the cellular traffic or not.
This is a joint work with Denis, Shinae, KyoungSoo and Yongdae.

## Slide 2: Mobile Devices as Post-PCs
Smartphones & tablet PCs for daily network communications
HotMobile’13, Jekyll Island, GA, USA
Notes: We use mobile devices such as smartphones and tablet PCs for most of daily network communications now.
We use smartphones to watch videos, listen to music, play games, do facebook, send emails, and so on.

## Slide 3: Mobile Devices as Post-PCs
Smartphones & table PCs for daily network communications
  Massive growth in cellular data traffic
HotMobile’13, Jekyll Island, GA, USA
2x increase
in one year!
Notes: As a result, we are seeing a massive growth in cellular data traffic in very short time.
Ericsson reported that just during last year, the usage of cellular data traffic has doubled in volume.
What is the side effect of this explosive growth?

## Slide 4: Cellular Traffic Accounting
Increase in cellular traffic bill
  Average: $71 per month (2011) – J.D. Power & Associates
Overage fee
  e.g., $15 per GB
HotMobile’13, Jekyll Island, GA, USA
AT&T | 1GB | 4GB | 6GB | 10GB | 15GB | 20GB
Mobile Share with Unlimited Talk & Text | $40 | $70 | $90 | $120 | $160 | $200
Verizon | 1GB | 2GB | 4GB | 6GB | 8GB | 10GB
Mobile Share with Unlimited Talk & Text | $50 | $60 | $70 | $80 | $90 | $100
= $43,377.92!
Notes: As people use more and more traffic, obviously they have to pay more. As of 2011, the average cell bill was $71 per month.
As we see with AT&T and Verizon, as people ask for more data, the price increases.
But the problem gets worse when you have to pay for overage fee.
Here we have one user who is subscribed to monthly data plan for 500MB. Instead of using just the given 500MB limit, she overused by 185GB. What’s the total cost? Over $43,000!
Certainly you don’t want that happen to you.
Then how could have this happened?? Let’s look at how the ISP actually charges you.

## Slide 5: 3G/4G Accounting System Architecture
Charging Data Record (CDR)
  Billing information (e.g., user identity, session elements, etc.)
Record traffic volume in IP packet-level
HotMobile’13, Jekyll Island, GA, USA
eNodeB
UE
RAN
NodeB
NodeB
RNC
3G UMTS
4G LTE
CN
BS
CGF
GGSN
SGSN
MME
P-GW
S-GW
Target Server
Internet
S-CDR
G-CDR
$
Question:
Should we account for TCP retransmissions?
Notes: Here’s the architecture of the cellular ISP.
When the client UE communicates with the target server, the packets flow through the ISP core network’s SGSN & GGSN.
The information for billing, CDR, is stored in the two GSNs during communication, then is transferred to the billing system where the actual accounting takes place.
And the basic unit for accounting is byte-per-byte IP packets.
Alright. So we now know that all IP packets flowing through the ISP are accounted.
Then here’s an interesting question. Should we then account for all retransmitted packets?

## Slide 6: Cellular Provider’s Dilemma: Charging TCP Retransmissions
Subscriber’s point of view
Pay for
application layer
data only!
Network condition
is not my concern
What’s
TCP
Retrans-mission?
Volume = File size
I don’t
care
Equal pricing
Not fair
ISP is evil
Notes: Let’s look at subscriber’s view on charging TCP retransmissions.
The main argument is that they should be charged for only the application layer data, which is the size of the content.
I don’t care what happens in the network. If this guy and I both watched the same movie content, we should be charged the same.

## Slide 7: Cellular Provider’s Dilemma: Charging TCP Retransmissions
Cellular ISP’s point of view
TCP retransmissions
still consume
resources
Retransmission =
another IP packet
Require system update
Question:
How serious is TCP retransmission in the real-world?
Notes: Then how about the cellular ISPs.
In their perspective, TCP retransmissions still consume their cellular network resources. To them, it’s just another IP packet.
Moreover, it would require a system that can accurately detect retransmission packets. They know that’s complex.
And… of course… not charging TCP retransmissions would mean losing money.
Then let’s see how much retransmission actually occurs in the real-world.

## Slide 8: Real-World TCP Retransmission Ratio
3G traffic of Korean cellular ISP on 2012/09/29 (9PM ~ 0AM)
  Mirror at one of 10 Gbps links below GGSN in Seoul
  134,574,018 flows
  6.64 TBs of IPv4 packets
1.89% of the flows show packet retransmissions
HotMobile’13, Jekyll Island, GA, USA
Chart: Retransmission Ratio
CDF
93%
Finding:
Charging TCP retransmissions may cause
legitimate users to suffer from high cellular bills!
Notes: For this, we measured the 3G traffic in one of the ISPs in Korea on 2012/09/29 (9PM~0AM) by mirroring one of 10 Gbps links below GGSN in Seoul.
The measurement consists of over 134 million flows with 6.64 TBs of IPv4 packets.
First, we see that just 1.89% of the flows showed any packet retransmissions. So most of people do not have to care about retransmissions.
We then drew a retransmission ratio CDF graph for the 1.89% flows that showed retransmissions.
Interestingly, some flows showed very high retransmission ratio up to 93%
So blindly charging TCP retransmissions may cause legitimate users to suffer from high cellular bills!
So we see that there is a potential problem in cellular accounting of TCP retransmissions.

## Slide 9: Previous Works
Peng et. al. [MobiCom’12 & CCS’12]
  “Toll-free-data-access-attack”
  Packets going through the DNS port are transferred free of charge
DNS lookups of 10,000 different domain names (Oct. 2012)
  Easy fix by analyzing packet payloads on DNS port
  Majority of ISPs prevent DNS tunneling attacks!
HotMobile’13, Jekyll Island, GA, USA
Cellular ISP | Result
2 US ISPs | Attack not possible
2 Korean ISPs | Attack not possible
1 Korean ISP | Attack possible via UDP-tunneling
Notes: There have been some related works that looked at other problems in cellular accounting.
Peng and others introduced a “toll-free-data-access-attack” in MobiCom and CCS last year.
They claimed that packets going through the DNS port were free of charge, enabling free data transfer via DNS tunneling.
In order to verify this, we ran a DNS-lookup of 10,000 different domain names in 2 US ISPs and 3 Korean ISPs.
We saw that only 1 ISP was vulnerable to UDP-tunneling. The 2 US ISPs have changed their policy to account for all packets on DNS port.
We were also surprised to see that 2 Korean ISPs were detecting tunneled packets.
It makes sense since preventing this attack is easy, just analyzing packet payloads on DNS port.

## Slide 10: Are ISPs Accounting Correctly?
Cellular ISP | Test Client Device
AT&T (US) | iPhone 4 (iOS 5.1.1 – 9B206)
Verizon (US) | iPad 2 (iOS 5.1.1 – 9B206)
SKT (South Korea) | Galaxy S3 (Android 4.0.4)
KT (South Korea) | Galaxy S3 (Android 4.0.4)
LGU+ (South Korea) | Galaxy S3 (Android 4.0.4)
HotMobile’13, Jekyll Island, GA, USA
Content transfer without packet loss
  All ISPs account for the proper amount
Retransmission test setup
Test Process
  Client: download a file via wget
  Server: retransmit packets via raw socket
  Compare captured volume with charged volume provided by ISP
Cellular ISP
raw
socket
wget
Notes: So the DNS attack is solved. Now let’s look at the general case. Are the ISPs accounting for normal data transmissions correctly?
We first check whether the ISPs account for base case where there is no packet loss, and confirm that they account for the proper amount.
Next, we experiment how ISPs are accounting for TCP retransmission packets.
For this test, we pick 2 ISPs from the US and 3 ISPs from South Korea and anonymize them by naming them with random numbers.
We have a client device which downloads a file from our modified HTTP server through the cellular network.
The server would then create retransmission packets by using a raw socket and sends them to the client.
For analysis, we capture the packets in the client and compare with charged volume provided by ISPs.

## Slide 11: Controlled Retransmission
Server intentionally sends the same packet for ‘n’ times
  (n = 10)
HotMobile’13, Jekyll Island, GA, USA
Data (Seq #: 1-1400)
ACK (Ack #: 1401)
Data (Seq #: 1-1400)
Dup. ACK (Ack #: 1401)
‘9’ Times
Data (Seq #: 1401-2801)
ACK (Ack #: 2802)
Notes: For a simple test, we create controlled retransmissions where our server intentionally sends the same packet for ‘n’ times.

## Slide 12: Controlled Retransmission
ISP-1, 2 do not account for retransmission packets
ISP-3, 4, 5 account for all retransmission packets!
Chart: Volume (KB)
| ISP-1 | ISP-2
Accounting | 1092.8083
Total = (1) | 11112.555
Chart: Volume (KB)
| ISP-1
Accounting | 1092.8083
(1) - Payload of Retransmitted Data Packet = (2) | 1524.1068
Chart: Volume (KB)
| ISP-1
Accounting | 1092.8083
(2) - Duplicate ACK = (3) | 1092.4771
Chart: Volume (KB)
| ISP-1
Accounting | 1092.8083
(4) - Data Packet Payload = (5) | 0
HotMobile’13, Jekyll Island, GA, USA
Chart: Volume (MB)
| ISP-2
Accounting | 14.9692
Total = (1) | 107.8105
Chart: Volume (MB)
| ISP-2
Accounting | 14.9692
(2) - Retransmitted Data = (3) | 14.9714
Chart: Volume (MB)
| ISP-2
Accounting | 14.9692
(3) - Duplicate ACK = (4) | 10.7651
ISP Accounting
Normal Data / ACK Packet
Duplicate ACK
Retransmitted Data Packet
1,092.8
1,092.5
1,524.1
11,122.6
Chart: Volume (MB)
| ISP-2
Accounting | 14.9692
(6) - Normal Data = (7) | -9.9999e-10
14.97
14.97
107.84
10.77
Notes: We see that ISPs 1 & 2 do not account for TCP retransmissions.
Let’s look at them in more detail by separating packets by each type.
Left graph shows the accounting volume of ISP-1 in KBs while the right graph shows the volume of ISP-2 in MBs.
The black bar shows the volume that the user actually has to pay.
We see that although both ISPs do not account for retransmission packets, their policy differs a little on what packets they do account for.
While ISP-1 does not account for duplicate ACKs, ISP-2 does.
What’s more interesting is that ISPs 3, 4 & 5 account for all retransmission packets, which means that in case of ISP-2’s test, ISPs 3, 4 & 5 will charge you for 108MB instead of 15MB.
This raises a vulnerability in cellular accounting.

## Slide 13: Usage-Inflation Attack
Malicious server intentionally retransmits TCP packets
Inflation possible even after connection teardown
HotMobile’13, Jekyll Island, GA, USA
Malicious Server
Core Network
Victim UE
Wired Internet
Cellular Networks
Request
Overcharge Victim UE
Packet 1
Packet 1
$
Packet 1
Packet 1
$
Packet 1
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Packet 1
$
Notes: ISPs 3, 4 & 5 are vulnerable to usage inflation attack.
In this attack, a malicious server can overcharge the victim client by intentionally retransmitting TCP packets.
The client sends …(Explain the attack)
What’s more problematic is that this attack is possible even if the client closes the session.
As a result, you would get a huge bill.

## Slide 14: Quasi Retransmission
Partial retransmission via incrementing window by one byte
  No directly repeated sequence numbers
HotMobile’13, Jekyll Island, GA, USA
Data (Seq #: 1-1400)
ACK (Ack #: 1401)
Data (Seq #: 2-1401)
ACK (Ack #: 1402)
Data (Seq #: 3-1402)
ACK (Ack #: 1403)
Notes: Now let’s turn our attention to ISPs 1 & 2. We want to verify whether they are really correctly detecting and not accounting for retransmission packets.
For this, we create packets that has partially-retransmitted payload by increasing the TCP send window only by one byte.
As a result, there will be no directly repeated sequence numbers nor duplicate ACKs.
However, the majority of the payload would be duplicates.

## Slide 15: Quasi Retransmission
Results
  ISP-1 does not charge TCP/IP header of partially retransmitted packets
  ISP-2 charges TCP/IP header of partially retransmitted packets
HotMobile’13, Jekyll Island, GA, USA
Chart: Volume (KB)
| ISP-1
Accounting | 560.9281
Total = (1) | 12694.2507
Chart: Volume (KB)
| ISP-1
Accounting | 560.9281
(1) - Payload of Retransmitted Data Packet = (2) | 911.7578
Chart: Volume (KB)
| ISP-1
Accounting | 560.9281
(3) - TCP/IP Header for Data Packet = (4) | 561.276
Chart: Volume (MB)
| ISP-2
Accounting | 7.565
Total = (1) | 104.6652
Chart: Volume (MB)
| ISP-2
Accounting | 7.565
(3) - Duplicate ACK = (4) | 7.5607
ISP Accounting
Normal ACK + Normal Data Payload
TCP/IP Header for Data Packet
Partially Retransmitted Data Payload
Chart: Volume (KB)
| ISP-1
Accounting | 560.9281
(3) - TCP/IP Header for Data Packet = (4) | 0
560.9
561.3
911.8
12,704.3
Chart: Volume (MB)
| ISP-2
Accounting | 7.565
(3) - Duplicate ACK = (4) | 0
7.56
7.56
104.67
Chart: Volume (MB)
| ISP-2
Accounting | 7.565
(4) - Normal ACK = (5) | 4.62
4.62
Question:
What happens if we can tunnel the packet
inside retransmission packets?
Notes: The results show that both ISPs correctly identify the partially-retransmitted payload and do not account for them.
But again, they have a slight different policy on accounting the TCP/IP header of partially-retransmitted packets.
…(Explain the result)
Great. So ISPs 1 & 2 correctly detect and do not account for retransmission packets.
But… let’s ask this question. What would happen if we can tunnel the retransmission packets without detection?

## Slide 16: Free-riding Retransmission Attack
Hide real traffic inside payload of TCP retransmission packets
  ISP inspects TCP header only, not the payload
HotMobile’13, Jekyll Island, GA, USA
Core Network
Malicious UE
Cellular Networks
Destination
Server
Wired Internet
TCP Tunneling
Proxy
Request
Packet 1
Fake TCP Hdr
Packet 1
Tunnel TCP Packet
Fake TCP Hdr
Packet 1
$
Packet 1
Packet 2
Fake TCP Hdr
Packet 2
Fake TCP Hdr
Packet 2
Packet 2
Packet 3
Fake TCP Hdr
Packet 3
Packet 3
Fake TCP Hdr
Packet 3
Notes: If this is possible, we can carry out a free-riding retransmission attack.
In this attack, we can hide the real traffic inside the payload of TCP retransmission packets.
…(Explain the attack)
We checked whether this attack is possible with ISPs that do not account for retransmission packets.

## Slide 17: Tunneling through Retransmission
Server sends the same header for ‘n’ times with different payload
  (n = 2)
HotMobile’13, Jekyll Island, GA, USA
Chart: Volume (KB)
| ISP-1
Accounting | 5469.3737
Total = (1) | 10982.8086
Chart: Volume (KB)
| ISP-1
Accounting | 5469.3737
(1) - Payload of Retransmitted Data Packet = (2) | 5704.431
Chart: Volume (KB)
| ISP-1
Accounting | 5469.3737
(2) - Duplicate ACK = (3) | 5483.3548
Chart: Volume (KB)
| ISP-1
Accounting | 5469.3737
(3) - TCP/IP Header for Data Packet = (4) | 5331.0762
Chart: Volume (MB)
| ISP-2
Accounting | 55.8106
Total = (1) | 107.5051
Chart: Volume (MB)
| ISP-2
Accounting | 55.8106
(2) - Retransmitted Data = (3) | 55.8082
Chart: Volume (MB)
| ISP-2
Accounting | 55.8106
(3) - Duplicate ACK = (4) | 53.6486
Chart: Volume (MB)
| ISP-2
Accounting | 55.8106
(4) - Normal ACK = (5) | 51.489
Chart: Volume (MB)
| ISP-2
Accounting | 55.8106
(4) - Normal ACK = (5) | 0
ISP Accounting
Normal ACK
TCP Tunneled Packet
Normal Data Packet
Duplicate ACK
10,992.8
5,272.3
55.81
5,704.4
51.49
53.65
55.81
107.51
Chart: Volume (KB)
| ISP-1
Accounting | 5469.3737
(4) - Data Packet Payload = (5) | 0
5,469.4
Finding:
ISPs do not account for TCP-tunneled retransmission packets!
5,483.4
Notes: In order to check for this, we create TCP-tunneled retransmission packets where the payload of retransmitted packets are different.
…(Explain the result)
We find that ISPs do not account for TCP-tunneled retransmission packets!
This is pretty intuitive since analyzing the payload of all packets would require lots of CPU cycles, a huge performance overhead.
In this paper, we suggest a number of solutions to mitigate this attack.

## Slide 18: Mitigation Techniques
Detection of abnormal retransmission
  Limit the number or ratio of retransmission packets per flow
   Small states per each flow
   False-positive alarm on legitimate flows
Deterministic DPI
  Compare the payload of all retransmission packets
   No false-positive alarm
   High system overheads due to buffer management
HotMobile’13, Jekyll Island, GA, USA
Notes: The simplistic way is to detect abnormal retransmissions by setting a threshold for number or ratio of retransmission packets per flow.
If a flow detects an abnormal retransmission, the ISP can then decide to either charge all retransmission packets or explicitly close the connection.
This method is advantageous in that it requires small states per each flow (such as number of retransmissions, etc.)
However, it could incur false-positive alarms on legitimate flows. We have already seen that even legitimate flows see retransmission ratio of up to 93%.
A more accurate solution is run deep packet inspection on all TCP flows by comparing the payload of all packets.
This method does not incur any false-positive alarm.
However, due to buffering of the entire payloads, it requires high memory overheads.

## Slide 19: Lightweight Solution : Probabilistic DPI
Inspect a part of the payload of retransmission packets
   Small memory requirements
  Minimal false-positives
Store n random locations per packet
  Sequence number as the index
  Random number generator to determine locations per each flow
  Compute the difference between n-byte sequences
HotMobile’13, Jekyll Island, GA, USA
Future Work:
Build a high-speed cellular traffic monitoring middlebox system
Notes: To reduce this overhead on memory requirements, we propose a lightweight solution called probabilistic DPI.
This stores and inspects only a part of the payload of retransmission packets.
It only requires small memory as well as minimal false-positives.
To extract the random bytes from the payload, we can use the sequence number as an index to the table that contains ‘n’ random locations.
We could determine these n-byte locations per each flow by using a random number generator with a secret number as a seed.
Once we have extracted some bytes from the same location, we can compute the difference between those n-byte sequences.

## Slide 20: Conclusion
Massive growth in cellular data usage
  Importance of accurate accounting of cellular traffic
Cellular ISP dilemma
  Should we account for TCP retransmissions packets or not?
Accounting policies of ISPs differ even in the same country
Vulnerabilities in current accounting system
  Usage-inflation attack
  Free-riding retransmission attack
Suggest possible solutions on free-riding retransmission attack
HotMobile’13, Jekyll Island, GA, USA
Notes: We have seen a massive growth in the cellular data usage.
However, the cellular ISPs are in a dilemma on whether to account for TCP retransmissions or not.
Through experiments, we see that no ISPs have perfect accounting policy for TCP retransmissions.
Some ISPs account for duplicate ACKs, some ISPs do not account for TCP headers of all partially-retransmitted payload packets.
Moreover, we have shown that whether we account for TCP retransmissions or not, ISPs are vulnerable to either usage-inflation attack or free-riding retransmission attack.
For future work, we suggest a probabilistic DPI system, which can accurately detect fake TCP retransmissions in high-speed.

## Slide 21: Thank You! Any Questions?
http://www.ndsl.kaist.edu
Volunteers Needed !
yhwan@ndsl.kaist.edu
HotMobile’13, Jekyll Island, GA, USA
Notes: We are looking for volunteer for measuring other ISPs on whether they account for TCP retransmissions.
If you are interested, please send an email to this address.

## Slide 22: Cellular Accounting Unit
Record traffic volume in the form of T-PDU
  Original IP packet
Move around GSNs via GTP-U tunnels
  Attach GTP-U header in front of T-PDU
HotMobile’13, Jekyll Island, GA, USA
GTP-U Header
IP Header
TCP
Header
Data Payload
T-PDU
GTP-U

## Slide 23: Unlimited LTE Data Plan
HotMobile’13, Jekyll Island, GA, USA
Cellular ISP | Price (per month) | Note | Throttling Volume
U.S. Cellular | $40 | No voice/text/tethering | -
T-Mobile | $70 / $90 | HSPA+ | -
Sprint | $79.99 | Small coverage | -
SKT | $101.34 | Data throttling | 18 GB
KT | $87.99 | Data throttling | 14 GB
 | $102.27 | Data throttling | 20 GB
 | $120.87 | Data throttling | 24 GB
LGU+ | $87.99 | Data throttling | 14 GB
 | $102.27 | Data throttling | 20 GB
 | $120.87 | Data throttling | 24 GB
Notes: As people use more and more traffic, obviously they have to pay more. As of 2011, the average cell bill was $71 per month.
Not only that, if the users who are subscribed to monthly data plan use up all of provided monthly volume, they need to pay huge amount of bill for extra volume used.
Many users try to overcome this problem by subscribing to unlimited data plans where the users pay for a fixed price regardless of how much traffic they consume.
However, this is not so simple. Here is a table of American and Korean ISPs that provide unlimited LTE data plans.
…(Explain table)
As a result, accurate accounting of cellular traffic usage is vital for normal users.